## Slide 1: Introduction to WOFRY
Transport of coherence in a beamline

## Slide 2
Introduction to WOFRY
Transport of coherence in a Beamline
Manuel Sanchez del Rio
srio@esrf.eu
Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
May 29th 2023
WOFRY

## Slide 3: Transport of coherence in a Beamline
Outline:
Basics of Partial Coherence in SR
Introduction to Coherent Mode Decomposition with 2D and 1D wavefronts
What is WOFRY
Gallery of exercises and examples
Gallery of results

## Slide 4: Basics

## Slide 5: From theory to software: ALL ABOUT LIGHT
Wavefront
Rays
FULLY COHERENT:
A WAVEFRONT IS ALWAYS COHERENT
FULLY INCOHERENT:
A RAY IS A PLANE WAVEFRONT
THE RAYS DO NOT INTERFERE

## Slide 6: Coherence – Basic concepts
Coherence: is the ability of a beam to be diffracted by objects (e.g. slits) producing a “diffraction pattern”
Diffraction pattern results from the interference of propagated electric fields
1 m
15 m
Ray tracing

## Slide 7
The electron emittance implies partial coherence
1 electron => Trajectory => Wavefront
Many identical electrons [filament beam] => Wavefront
Many non-identical electrons: multiple wavefronts

## Slide 8: 4th generation synchrotron sources
X-FEL
  Bunch length ~ wavelength emitted so emission from different electrons add coherently – transversal (spatial) and longitudinal (time) coherence
Storage Ring
  Bunch length >> wavelength so emission from electrons add incoherently.
  Reduce the emittance from 3rd generation with the aim of becoming “diffraction limit” sources, i.e., natural emission << electron size. DLSR? Better ultra low emittance SR

## Slide 9: ESRF and EBS LATTICES
High Beta:
bx = 37.59 m
by = 2.95 m
sx = 415.0 mm
sy = 3.43 mm
sx’= 10.3 mrad
sz’=1.16 mrad
Low Beta:
bx = 0.35 m
by = 3.0 m
sx = 50.4 mm
sy = 3.44 mm
sx’= 107.2 mrad
sz’=1.16 mrad
EBS (S28D):
bx = 6.90 m
by = 2.64 m
sx = 30.2 mm
sy = 3.64 mm
sx’= 4.37 mrad
sz’=1.37 mrad
Horizontal emittance = 4000 pm Horizontal emittance = 137 pm
ESRF Double Bend Achromat (ESRF-1) -> Multi-bend achromat (EBS)

## Slide 10: EBS – ESRF U18 2m @ 8 keV L=2m observed at 30m
  Big increase of brightness and transverse coherence

## Slide 11: ALS-U
Linac
(existing)
Booster
(existing)
Transfer lines
  New 2.0 GeV 9BA storage ring in existing tunnel optimized for low emittance and high soft x-ray brightness and coherent flux
  New 2.0 GeV accumulator ring for full-energy swap-out injection and recovery of bunch trains
  New full-length undulators optimized for high coherent flux
Today’s ALS
Future ALS
Electron Beam Profiles

## Slide 12: All we need is Cross Spectral Density
Coherent length
Can be defined
from some cuts

## Slide 13: Coherent Mode Decomposition
2D functions
4D function
W ~ 108 – 1012 (Gb-Tb)
Store: m x N x N; Propagate: 2D integrals
10D function (3x3+1)
Fix E and z => 4D
Still W too big to calculate/store
M Glass, M Sanchez del Rio, EPL Europhysics letters (2017)
http://dx.doi.org/10.1209/0295-5075/119/34004
Eigenfunctions:
Modes
Eigenvalues:
Weights or intensities

## Slide 14: COMSYL (Coherent Modes for Synchrotron Light)
COMSYL https://github.com/mark-glass/comsyl
OASYS
Calculate CSD
Coherent mode decomposition
Propagate CSD along the beamline
Rediagonalize CSD
K.-J. Kim Proc. SPIE 0582 (1986)
Diagonalize M with iterative solver slepc
Large memory.
Parallel computers using MPI.
Large clusters (ESRF). Cloud computing (AWS, etc.)
Friedholm equation:

## Slide 15: Benefits of Coherent Mode Decomposition
Modes (eigenfunctions):
Orthonormal
They can be propagated as simple wavefronts
Weights (eigenvalues):
Real numbers
Strictly decreasing
The sum is the intensity
Fully coherent if and only if there is only a single mode
Occupation (normalized weight) =
Coherent Fraction = occupation of 0th mode:
Coherent Fraction
EBS 2.8%
ESRF-EBS (17 keV)
https://youtu.be/h24RrJZaQ80

## Slide 16: Important: A mode propagated is not longer a mode
Each mode propagate like a wavefront so one can build the CSD at any point by propagating the modes to that point:
At
Propagate modes at to another point :
Build the propagated CDS:
Note that are not modes as they are not longer orthonormal (they have been cropped and transformed)
We do again a CMD of to compute the new eigenvalues and eigenvectors and therefore the new CF.

## Slide 17: Everything is much simpler in 1D:
Horizontal W(x1,x2) Vertical W(y1, y2)
A fast and lightweight tool for partially coherent beamline simulations in fourth-generation
storage rings based on coherent mode decomposition. J. Synchrotron Rad. 29, 1354–1367 (2022)
Sanchez del Rio, M., Celestre, R., Reyes-Herrera, J., Brumund, P. & Cammarata, M..
DOI: http://dx.doi.org/10.1107/S1600577522008736
CMD WITH WOFRY (EBS U18 2.5m 7 kev)

## Slide 18: WOFRY Wave Optics FRamwork in pYthon
WOFRY is the OASYS framework for waveoptics calculations.
From the software engineering point of view, it provides a generalization (or abstraction) of a software tool for wave optics, combining the component definitions from SYNED with the abstract declaration of wavefronts and propagators https://doi.org/10.1117/12.2274232, and defines a mechanism for interfacing a wave optics codes (e.g., SRW, WISE etc.) in OASYS [package: WOFRY]
From the physics point of view, it provides native implementations of simple wavefronts (e.g., plane waves, spherical waves, Gaussian sources), makes 1D coherent mode decomposition, and include free space propagators and optical elements for prototyping optical systems (in 1D and 2D). [package: WOFRYIMPL]

## Slide 19: WOFRY
Sources Optical elements Tools

## Slide 20: Gallery of exercises & examples (afternoon session)

## Slide 21: Diffraction by slits (full coherence)
Aperture=0.4 mm, E=17225 eV, D=5cm
F=D
F=D/2
F=D/2
Converging spherical +
Propagation (D)
Plane + Lens (F=D)+ Propagation (D)
Spherical divergent+ Lens (F=D/2)+ Propagation (D)
Gaussian+ Propagation(D)+ Lens (F=D/2)+ Propagation (D)
21

## Slide 22: 2D Oversimplified Beamline (APS-ISN)
The diffraction by a DxD square aperture of a collapsing spherical wavefront has an intensity distribution proportional to sinc2(kDx/2f ) sinc2(kDy/2f), where k=2π/λ, x(y) is the horizontal (vertical) coordinate, and f is the distance aperture-focus (D/f is the divergence). Considering that the FWHM of sinc2(x) is approximately 2.78, one obtains FWHM=0.885 * wavelength / divergence
Size FHHM 0.0148872 x 0.016168 um
Theoretical consideration

## Slide 23: Example: Gain coherence by using a slit ESRF U17 @ 15 keV
CFv=0.97
CFv=0.54
CFh=0.53
CFh=0.07
Horizontal
Vertical
50x50 mm2
Modes Cumulated occupation
Modes Cumulated occupation
CF= CFh x CFv:
Source: 0.038
Image: 0.51
MODEL 3

## Slide 24: 1D model of ISN Beamline (25 keV)
CF: 14%
CF: 38%
CF: 88%
CF: 52%
CF: 90%
CF: 99%
14 mm
4 mm

## Slide 25: ALS-FLEXON: CORRECTION OF THERMAL DEFORMATION WITH ADAPTIVE OPTICS
LN cooling Cutler et al. http://dx.doi.org/10.1107/S1600577520009522)
M. Sanchez del Rio et al, JSR 2020
http://dx.doi.org/10.1107/S1600577520009522
M1: 819μm
M3: 1630 μm
Sample: 3.8 μm
Water cooling
(CF ~ 0.8 with a 4 m undulator at 230 eV)

## Slide 26: Gallery of results

## Slide 27: EBS vs ESRF1 : Coherence fraction with COMSYL
M Glass, M Sanchez del Rio, EPL Europhysics letters (2017)
http://dx.doi.org/10.1209/0295-5075/119/34004

## Slide 28: COHERENCE FRACTION MODIFICATION BY SLITS
13% (H)
58% (V)
EBS U18 L=2.5m
Sanchez del Rio, M., Celestre, R., Reyes-Herrera, J., Brumund, P. & Cammarata, M..
J. Synchrotron Rad. 29, 1354–1367 (2022)
DOI: http://dx.doi.org/10.1107/S1600577522008736

## Slide 29: ALS-U U38 source 806 eV (COMSYL CMD)
m=0
m=0
m=9
m=8
m=7
m=6
m=4
m=5
m=3
m=2
m=1
m=19 (ice crystal)
m=32 (mask)
m=43 (clock)

## Slide 30: Beam focus modifications by cropping partially coherent X-ray beams
p0
p1
Sanchez del Rio, M., Celestre, R., Reyes-Herrera, J., Brumund, P. & Cammarata, M.
EPL 140 55001 (2022) DOI https://doi/org/10.1209/0295-5075/aca4ef

## Slide 31: Singularities in the phase of the cross spectral density
COMSYL 1.4-m-long U18 EBS (6 GeV, 147 pm rad emittance)
Eo = 17.226keV (K =0.411)
Intensity (spectral density)
First coherence mode
Fix a point
D Paganin, M Sanchez del Rio, Phys Rev A (2019)
http://dx.doi.org/10.1103/PhysRevA.100.043813

## Slide 32: Propagated BEAM: DIFFERENT TYPES OF SINGULARITIES APPEAR
Domain walls
Coherence
vortices
a,b, g
Halo of CSD speckle
Vortex-antivortex hi,jk
D Paganin, M Sanchez del Rio, Phys Rev A (2019)
http://dx.doi.org/10.1103/PhysRevA.100.043813

## Slide 33: Thank you!
OASYS Workspaces for exercises and examples: https://drive.google.com/drive/folders/1tRkhSphrNybnI_-rflk7bG2dUEJ9CVuZ?usp=drive_link

## Slide 34: Extra slides

## Slide 35: Propagators
1D
2D
Fresnel
Fresnel (convolution)
Integral
Fresnel Zoom
Fresnel Zoom Scaled

## Slide 36: Zoom Propagator
G. Pirro, Master Thesis (2017)
https://github.com/oasys-kit/documents/blob/master/zoom_propagator_pirro_thesis.pdf

## Slide 37: SIMPLE CASE: 1D Gaussian SHELL-MODEL
Both intensity (Spectral Density) and correlation (Spectral Degree of Coherence) are Gaussians
sI>>sm the source is mostly incoherent (quasi homogeneous)
sI<<sm is mostly coherent
I
I
In 2D (H x V)
2D Hermite-Gaussian or
TEMnm modes
Eigenvalues
Eigenfunctions
(Hermite-Gaussian modes)
Magic property: Propagation invariance
In the first mode (Gaussian) :

## Slide 38: The spectrum of coherent modes
Coherent: b>>
incoherent
In general we cannot apply Gaussian Shell-model to synchrotron
b<<
Eigenvalues
Mode occupation:
Coherent fraction:

## Slide 39: Coherence – Longitudinal and transversal
Longitudinal or Temporal Coherence: depends on the monochromaticity of the source (describes the correlation or predictable relationship between waves observed at different moments in time)
Transversal Coherence: Depends on the source geometry (correlation between waves at different points in space)
We need at least TWO waves for defining coherence parameters